## Slide 1: Development of Barrier Bucket RF Systems for ESR and SIS100
M. Frey, 14. June 2018

## Slide 2: outline
motivation/history at ESR
ESR BB system
  requirements
  theory of operation
  choice of ring core material
ESR BB cavity design
  prototype ring core impedance measurement+modeling
  PSpice simulation of full cavity
ESR BB cavity properties
ESR BB pre-distortion
ESR BB signal generation
ESR BB full system results
ESR BB outlook
SIS100 BB system

## Slide 3: motivation
RF pulses create potential barriers
barrier creation allows longitudinal beam manipulation, e.g. confinement of a bunch
when barriers are moved, beams can be compressed -> intensity increases
multiple injections between compression operations lead to further intensity increase („longitudinal stacking“)
J. Harzheim, Temf, TU Darmstadt
voltage
potential
bucket
bucket height

## Slide 4: demonstration at ESR
ferrite acceleration cavities were used with single sine + offset pulses
gap voltage
beam signal
hardly feasible due to extreme sensitivity concerning pulse parameters
G. Schreiber, LRF department, GSI
C. Dimopoulou, BCO department, GSI
development of a specialized BB cavity

## Slide 5: outline
motivation/history at ESR
ESR BB system
  requirements
  theory of operation
  choice of ring core material
ESR BB cavity design
  prototype ring core impedance measurement+modeling
  PSpice simulation of full cavity
ESR BB cavity properties
ESR BB pre-distortion
ESR BB signal generation
ESR BB full system results
ESR BB outlook
SIS100 BB system

## Slide 6: ESR requirements
single sine pulses of T1=200 ns (fBB=5 MHz)
pulse amplitude
flexible control of amplitude and repetition period T2 at injection energy: 4-400 MeV (between frep=250 kHz and frep=2 MHz)
symmetry and low ringing

## Slide 7: ESR cavity design – theory of operation
H. Klingbeil, Temf, TU Darmstadt
cavities with ring cores are transformers: ring core = iron core, housing = secondary winding, gap capacity = load
ring cores are a lossy inductance defined by geometry and complex µr
ring core inductance L, resistance R and gap capacity C form RLC circuit
loss effects in ring cores described by (~R) -> define oscillation damping -> bandwidth

## Slide 8: ESR cavity design – ring core material
ferrites: high Q-value -> narrowband cavities 
iron-based nanocrystalline Magnetic Alloy (MA) ring cores: very low Q-value -> broadband cavities 
Hitachi Metals Ltd.
cores are wound from thin ribbon: side surfaces are roughly textured because layers tend to misalign (important for cooling)

## Slide 9: outline
strategy: ring cores dominate cavity –> analyse prototype core to enable simulation of full cavity -> obtain amplifiers load impedance
motivation/history at ESR
ESR BB system
  requirements
  theory of operation
  choice of ring core material
ESR BB cavity design
  prototype ring core impedance measurement+modeling
  PSpice simulation of full cavity
ESR BB cavity properties
ESR BB pre-distortion
ESR BB signal generation
ESR BB full system results
ESR BB outlook
SIS100 BB system

## Slide 10: ESR cavity design – impedance measurement and PSpice modeling
impedance measurement of prototype core in test box
subtraction of test box influence (estimated with CST simulation)
identification of lumped-element equivalent circuit using „vector-fitting“ algorithm
J. Harzheim, H. Klingbeil, Temf, TU Darmstadt
1 ring core at 5 MHz: |Z|≈200 Ω
P. Hülsmann, RRF department, GSI

## Slide 11: ESR cavity idea
4 ring cores connected in parallel
-> gap voltage = 4 x voltage at load
one cavity per pulse (2 in same housing)
P. Hülsmann, RRF department, GSI

## Slide 12: ESR simulation of full cavity
cavity
1 m cable
coupling loops
sufficient matching between amplifier and cavity at 5 MHz
at 5 MHz and |Z|=25 Ω, U=4x225 V =900 V possible with 1 kW
Chart: f/MHz
Chart: f/MHz
J. Harzheim, H. Klingbeil, Temf, TU Darmstadt
satisfying results
production approval

## Slide 13: ESR cavity design – CAD and production
C. Christoph, RRF department, GSI
based on extensive testing with ARD broadband test cavity
amplifiers
air cooling
very short beam pipe requested (for Schottky pick-up on same base-frame)
large ESR beam pipe diameter -> little space for ring core material
power range of amplifiers 1 kW -> air cooling necessary
unspectacular but huge milestone!

## Slide 14: outline
motivation/history at ESR
ESR BB system
  requirements
  theory of operation
  choice of ring core material
ESR BB cavity design
  prototype ring core impedance measurement+modeling
  PSpice simulation of full cavity
ESR BB cavity properties
ESR BB pre-distortion
ESR BB signal generation
ESR BB full system results
ESR BB outlook
SIS100 BB system

## Slide 15: ESR cavity properties
measurement result:
frequency response results in distortion of input voltage
pre-distortion of signals is necessary
simulation without gap voltage divider

## Slide 16: LLRF - pre-distortion of signals
Chart: f/MHz
Chart: f/MHz
1. measure transfer function H
2. calculate Fourier-coefficients of pre-distorted signal
3. transformation to time-domain + application
single-sine signal
linear, time-invariant system, periodic signal
periodic signal -> one cavity per pulse for moving barriers
gap voltage accuracy depends on system bandwith (=number of transmittable bn)

## Slide 17: LLRF - non-linear predistortion
J. Harzheim, H. Klingbeil, Temf, TU Darmstadt
a) Nonlinearity is modeled by a static nonlinearity at the amplifier input, while the rest of the system is modeled linear (Hammerstein model)
b) Optimization (iterative) of input signal for specific working point
Chart: normalized input voltage/%
| -107.03363914373089 | -103.97553516819571 | -100.91743119266054 | -97.859327217125383 | -94.801223241590222 | -91.743119266055047 | -85.62691131498471 | -79.510703363914374 | -73.394495412844037 | -67.278287461773701 | -61.162079510703357 | -55.045871559633028 | -48.929663608562691 | -42.813455657492355 | -36.697247706422019 | -30.581039755351679 | -24.464831804281346 | -18.348623853211009 | -12.232415902140673 | -6.1162079510703364 | 6.1162079510703364 | 12.232415902140673 | 18.348623853211009 | 24.464831804281346 | 30.581039755351679 | 36.697247706422019 | 42.813455657492355 | 48.929663608562691 | 55.045871559633028 | 61.162079510703357 | 67.278287461773701 | 73.394495412844037 | 79.510703363914374 | 85.62691131498471 | 91.743119266055047 | 94.801223241590222 | 97.859327217125383 | 100.91743119266054 | 103.97553516819571 | 107.03363914373089
amplifier A | -2415 | -2347 | -2278 | -2219 | -2150 | -2083 | -1944 | -1814 | -1674 | -1542 | -1399 | -1253 | -1109 | -970.3 | -826.1 | -687.7 | -549 | -409.3 | -273.4 | -136.7 | 136.7 | 273.2 | 415.1 | 552.7 | 690.2 | 826 | 965.7 | 1104 | 1242 | 1385 | 1522 | 1662 | 1804 | 1942 | 2070 | 2141 | 2208 | 2273 | 2339 | 2407
Gerade_BBL | -2413.71 | -2344.78 | -2275.85 | -2206.92 | -2137.99 | -2069.06 | -1931.2 | -1793.34 | -1655.48 | -1517.62 | -1379.76 | -1241.9 | -1104.04 | -966.18 | -828.32 | -690.46 | -552.6 | -414.74 | -276.88 | -139.02 | 136.7 | 274.56 | 412.42 | 550.28 | 688.14 | 826 | 963.86 | 1101.72 | 1239.58 | 1377.44 | 1515.3 | 1653.16 | 1791.02 | 1928.88 | 2066.74 | 2135.67 | 2204.6 | 2273.53 | 2342.46 | 2411.39
amplifier B | -1792 | -1724 | -1653 | -1583 | -1514 | -1439 | -1364 | -1287 | -1208 | -1128 | -1043 | -961 | -875 | -789 | -704 | -617 | -529 | -441 | -353 | -264.5 | -170 | -85 | 85 | 171 | 265.5 | 354.5 | 447 | 535 | 624 | 711 | 798 | 886 | 970 | 1056 | 1142 | 1224 | 1306 | 1383 | 1459 | 1533 | 1610 | 1684 | 1755 | 1824
Gerade_2500 | -1981.1667 | -1891.3333 | -1801.5 | -1711.6667 | -1621.8333 | -1532 | -1442.1667 | -1352.3333 | -1262.5 | -1172.6667 | -1082.8333 | -993 | -903.1667 | -813.3333 | -723.5 | -633.6667 | -543.8333 | -454 | -364.1667 | -274.3333 | -184.5 | -94.6667 | 85 | 174.8333 | 264.6667 | 354.5 | 444.3333 | 534.1667 | 624 | 713.8333 | 803.6667 | 893.5 | 983.3333 | 1073.1667 | 1163 | 1252.8333 | 1342.6667 | 1432.5 | 1522.3333 | 1612.1667 | 1702 | 1791.8333 | 1881.6667 | 1971.5
amplifier C | -1552 | -1552 | -1552 | -1536 | -1504 | -1440 | -1368 | -1304 | -1240 | -1170 | -1092 | -1028 | -965 | -890 | -814.5 | -740 | -660 | -619.5 | -582 | -498 | -415 | -334 | -250.5 | -208.5 | -167 | -83.5 | -42 | 42.5 | 83.5 | 167 | 208.5 | 250.5 | 334 | 420 | 504 | 585 | 626.5 | 664 | 744 | 819 | 895 | 965 | 1028 | 1092 | 1170 | 1240 | 1304 | 1368 | 1432 | 1496 | 1544 | 1584 | 1600 | 1616
Gerade_1000 | -1998 | -1914.7143 | -1831.4286 | -1748.1429 | -1664.8571 | -1581.5714 | -1498.2857 | -1415 | -1331.7143 | -1248.4286 | -1165.1429 | -1081.8571 | -998.5714 | -915.2857 | -832 | -748.7143 | -665.4286 | -623.7857 | -582.1429 | -498.8571 | -415.5714 | -332.2857 | -249 | -207.3571 | -165.7143 | -82.4286 | -40.7857 | 42.5 | 84.1429 | 167.4286 | 209.0714 | 250.7143 | 334 | 417.2857 | 500.5714 | 583.8571 | 625.5 | 667.1429 | 750.4286 | 833.7143 | 917 | 1000.2857 | 1083.5714 | 1166.8571 | 1250.1429 | 1333.4286 | 1416.7143 | 1500 | 1583.2857 | 1666.5714 | 1749.8571 | 1833.1429 | 1916.4286 | 1999.7143
problem with linear pre-distortion: amplifier characteristic
no datasheet value depicts this characteristic -> amplifier selection by testing

## Slide 18: outline
motivation/history at ESR
ESR BB system
  requirements
  theory of operation
  choice of ring core material
ESR BB cavity design
  prototype ring core impedance measurement+modeling
  PSpice simulation of full cavity
ESR BB cavity properties
ESR BB pre-distortion
ESR BB signal generation
ESR BB full system results
ESR BB outlook
SIS100 BB system

## Slide 19: LLRF – re-triggering
Tabor AWG
DDS
(h=1)
Tabor AWG
TRG
RD
SCU
DAC
RAMP
CONV.
PC
when barriers are moved, consecutive pre-distorted waveforms may overlap
signal generation must detect new trigger while output still active
-> 2 alternating signal generators
produce alternating trigger pulses
playback of every 2nd waveform
signal combination
K. Groß, H. Klingbeil, Temf, TU Darmstadt

## Slide 20: ESR BB system – full system results I
linear pre-distortion:
Ub=520 V
good quality
non-linear pre-distortion:
Ub=800 V
improvement in ringing after pulse
symmetry insufficient (internal amplifier limitation?)
J. Harzheim, Temf, TU Darmstadt

## Slide 21: ESR BB system – full system results II
full system works as intended! -> installation appproval
K. Groß, Temf, TU Darmstadt
two revolution periods are shown
here barriers are created at equal phase angle (amplitude doubles)
one barrier is shifted by 180° in both directions
phase shifting of moving barriers demonstrated with full system (manual data supply from PC to SCU)

## Slide 22: ESR BB system – status + outlook
status:
function of full system demonstrated
pulse amplitude Ub=520 V with high quality achieved (1 kW amplifier)
installation in ESR finished
to do:
software development for unit controller (task: e.g. calculation of pre-distorted waveforms, control of signal generators)
adaption of control system connection (e.g. phase ramp in FESA-class for ramped-devices?)

## Slide 23: outline
ESR BB system
SIS100 BB system: pre-development phase
  requirements
SIS100 BB cavity design
  oil cooling
SIS100 BB power amplifier design
SIS100 BB simulation results
  frequency domain
  time domain
SIS100 BB outlook
procurement starts 2019

## Slide 24: SIS100 requirements
creation of 2 barriers in two empty buckets -> single sine pulses of T1=666 ns (fBB=1.5 MHz)
flexible control of amplitude and repetition period T2 between frep=110 kHz and frep=270 kHz
pulse amplitude =15 kV
maximum beam impedance 1000 Ω (cavity+amplifier)
cavity length <1.3 m, but only 1.0 m for housing (due to feasibility of flange mounting)
usability of identical cavities and amplifiers for SIS100 Longitudinal Feedback workpackage

## Slide 25: SIS100 BB cavity design
design goals:
broadband behaviour (-> MA cores)
voltage gradient 15 kV/m (MA cores)
matching with tetrode amplifier at tetrode´s working point
cavity´s resonance frequency at or below barrier-bucket frequency fBB
=> very similar to SIS18 h=2 cavity requirements!
working hypothesis:
use h=2 cavity with less MA cores in order to increase resonant frequency
C. Christoph, RRF department, GSI

## Slide 26: SIS100 BB – oil cooling
due to magnetic loss effects, ring cores heat up during operation
heat conductivity in FT-3M is anisotropic
heat can only be removed through side surface, which is not flat
insufficient heat transfer to cooling disks or air makes direct liquid cooling (oil) necessary
P. Hülsmann, RRF department, GSI

## Slide 27: outline
ESR BB system
SIS100 BB system: pre-development phase
  requirements
SIS100 BB cavity design
  oil cooling
SIS100 BB power amplifier design
SIS100 BB simulation results
  frequency domain
  time domain
SIS100 BB outlook
strategy:
PSpice simulation of planned SIS100 BB cavity system
comparison with measurements from mock-up of SIS100 BB cavity (with h=2 components)

## Slide 28: SIS100 BB power amplifier design
required signal quality -> class A amplifier (to avoid distortion in push-pull configuration)
tetrode capable of the expected anode dissipation power at working point above 15 kV -> Thales TH555
compensation of anode currents by opposing winding directions of coupling loops
P. Hülsmann, RRF department, GSI

## Slide 29: SIS100 BB simulation results – frequency domain
Chart: f/MHz
Chart: f/MHz
cavity without amplifier (measured at h=2 cavity):
tetrode model includes non-linearity
deviations now understood
sufficient matching between cavity and tetrode (Ri≈1500Ω)
resonant frequency fr≈1.5 MHz
cavity: shown is one of four ring core stacks
power amplifier

## Slide 30: SIS100 BB simulation results – time domain
Chart: t/µs
Chart: t/µs
desired pulse amplitude of 15 kV is achieved (7.5 kV across each gap)
ringing at the pulse´s end is below 5% even with linear pre-distortion
input voltage in time domain (linear pre-distortion, 0.02-30 MHz):
desired bandwidth for input signal transmitting components: from 20 kHz to 30 MHz

## Slide 31: SIS100 BB status and outlook
Technical Concept document finished
considerable effort was made to reduce technical risks by investigating (mostly at ARD broadband test cavity):
  frequency dependent ring core properties
  cavity bandwidth
  ring core cooling
  frequency- and time-domain simulations of full cavity/amplifier system
  impedance reduction by cavity detuning
  beam loading (effect of DC-fraction)
  signal generation (LLRF system)
Technical Concept proved feasible through all tests (15 kV, <5% ringing expected with non-linear pre-distortion)
Detailed Specification 95% finished
start of procurement is planned for June 2019

## Slide 32: Thanks to all contributors

## Slide 33: Development of Barrier Bucket RF Systems for ESR and SIS100
M. Frey, 14. June 2018
Thank you for your attention

## Slide 34: Appendix - gap voltage measurement
distortion in measurement chain directly alters gap voltage signal
high effort necessary to reach convenient frequency-response
high impedance part kept as short as possible (reduce reflections)
130 m ½‘‘ Cellflex: 5% distortion
2000 m optical fiber: 2% distortion (but synchronisation with SIS18 not possible yet)